Elevating work platform routine and pre-harvest inspection checklist

| Item | Type of check | Completed Initial and date |
| --- | --- | --- |
|  | Visual | Functional |  |
| Check fluid levels, engine oil, hydraulic oil, coolant, fuel | X |  |  |
| Check service due date, check and clean filter(s) as required | X |  |  |
| Check exhaust for damage or holes that may contribute to excessive noise | X |  |  |
| Visually check hydraulic system, hoses and pipes for leaks (look for fresh oil stains on ground), check pipes and hoses are secured to prevent damage | X |  |  |
| Check tyre inflation pressures, condition of tyres and wheels and wheel nut tension. Check wheel ballast if fitted. | X |  |  |
| Grease or lubricate pivot points and moving parts as required | X |  |  |
| Check platform gate locking systems | X | X |  |
| Check condition of padding on the platform top rail to prevent impact injury | X |  |  |
| Check all controls, linkages and cables are free from damage, return to neutral and operate smoothly and freely (e.g. engine speed, forward/reverse, luffing and slewing, steering, emergency stop and emergency lower controls) | X | X |  |
| Check placards, decals, warnings and control markings are fitted and readable. Check manual is available. | X |  |  |
| Visually check stress areas such as welds on the boom mounts, boom section, hydraulic cylinder mounts, basket mounts and levelling bars for signs of cracking | X |  |  |
| Check pivot pins are secure and retainers are fitted | X |  |  |
| Check for loose or missing parts | X |  |  |
| Check wiring and cables are secured to prevent damage, check battery is secure | X |  |  |
| Check drive system is operational including brakes are working | X | X |  |
| Check for unauthorised modifications | X |  |  |
| Check fitted auxiliary systems (e.g. air compressors) | X |  |  |